## Slide 1
Self illuminated traffic signs

## Slide 2
Insufficient exposure to the curve slope section
Particulate matter in the rain, fog and haze air
City roads and other can not use high beams
Reverse light environment
Commercial lighting, environmental light is complex
Traditional signs rely on reflecting the light on the sign surface to provide nighttime vision
When the light cannot reach the surface of the sign, it cannot provide the night visual effect
The deficiency of the traditional sign

## Slide 3
Add supplementary light lamps and lanterns
Install light lamps with uneven illumination at night; shadows during the day
The rod needs to be redesigned and made, and the power consumption is relatively high
America
Europe
Hong Kong

## Slide 4
Apply the self illuminated sign
Shortly after the appearance of LED lamp beads, they were applied to the field of traffic signs to improve the recognition of signs
Dot matrix: use LED to outline the text, pattern; panel display type: use LED as the light source to project the pattern
The dot matrix
Panel type
Japan-Panel-type
USA- -dot matrix

## Slide 5
Development course of road traffic signs
Reflective film was born
In the early 20th century
The 1960s
In 2014,
Now
General Electric Corporation develops LED light-emitting diodes
Seckang began developing LED panels to display active light road traffic signs
New technologies such as the Internet, cloud computing and big data are booming
Inverse reflective traffic signs
Dot-matrix self illuminated sign
Panel displays the active luminescence sign
Intelligent and connected traffic signs

## Slide 6
Dot-matrix self illuminated traffic sign
Baseboard
Sign the panel-punch the hole
White reflective film-holes punched
Red reflective film-punched holes
Black reflective film- -with punched holes
LED lamp beads + a lens
Frame profile

## Slide 7
But there is glare, can only outline the pattern, text frame, can not clearly display the content of the sign
Low power consumption, low cost, the lamp bead can change color temperature, more suitable for temporary signs
An example of a dot-matrix self illuminaterd traffic sign

## Slide 8
Full transmission self illuminated traffic sign
Baseboard
LED light source board
The light plate
White high-light transmittance reflective film
Red reflective film
Black reflective film
Frame profile

## Slide 9
The night display effect is good, suitable for the ban, instructions, warning and other floor color has the legal meaning of the small sign
Examples of Full transmission self illuminated traffic sign
Limited by the size and structural strength of the transparent plate, it is not suitable to make the surface area too large

## Slide 10
Semi-transparent self illuminated traffic sign
Baseboard
LED light source board
Aluminum plate carved hollow-out text
Mosaic light transparent plate
Apply a whole white high-light transmittance reflective film
Text or pattern hollow-out reflective film
Frame profile

## Slide 11
Text, pattern and other information and the bottom plate contrast effect is obvious, has a better visual recognition effect
Can control the cost, power consumption and process difficulty
Examples of semi-transparent self illuminated traffic sign

## Slide 12
self illuminated traffic sign features
The self illuminated traffic sign has more balanced advantages in effect, cost, power consumption and other aspects
Recognize the effect | self illuminated | lattice | exterior lighting | retro reflection
cost of construction | exterior lighting | self illuminated | The dot matrix | retro reflection
power dissipation | exterior lighting | self illuminated | The dot matrix | retro reflection
Complex degree of process | self illuminated | The dot matrix | exterior lighting | retro reflection

## Slide 13
applied code
type | LED self illuminated traffic sign |  | The dot matrix
 | semi-transparent type | Full transmission type | 
applied code | T / CSIA001-2018 Panel Display Active Light Traffic Sign |  | GB / T31446-2015 LED Active Luminous Road Traffic Sign
Reflective film selection | Class IV (class V white film transmittance effect is poor), white panel part transmittance of 25% |  | Not higher than Class IV
supply electricity | Electric supply | Mans (higher solar cost) | UPDATE, solar
power dissipation | ≤20W/m2 | ≤32W/m2 | ＜10W
weight | ≤22±3kg/m2 |  | -
install | As with ordinary signs, the poles that meet the requirements of GB / T23827-2009 Road Traffic Sign Board and Support Parts can be installed |  | 
Investment benefit | From the perspective of traffic safety economics, the VE value can reach 60-105 times and 3-5 times of traditional reflective signs (Test and evaluation of applying active luminous technology to improve road traffic safety in Tongji University 》) |  | 
Visual effect | (When the surface illumination of the sign environment is 100 Lx, the sign is automatically lit) The effective visual distance at night is 200m |  | 

## Slide 14
Development direction of engineering and technology field
GB 5768.2 Adopt (active) luminous type according to the terrain and sunshine conditions
GA / T 1548 Guide to the Setting of Active Lighting Signs on Urban Roads puts forward the scene of applicable active luminous signs
T / CECS 626-2019 Standard for Setting Urban Underground Road Traffic Signs and Marines shall be adopted by China Engineering Construction Standardization Association
The revised GB 50688 "Design Code for Urban Road Traffic Facilities" and GB 51038 "Code for Setting up Urban Road Traffic Marks and Line Marines" will add some sections of urban expressways and urban roads, and set up active luminous road traffic signs
Technical Regulations for Setting highway LED Traffic Signs submitted for review by China Engineering Construction Association
Application trend of the active luminescence sign in the standard specification
The field of engineering technology has also begun to pay attention to the problems of traditional traffic signs

## Slide 15
Intelligent network sign
Real-time risk perception and prompt
Real-time warning
Combine path guidance with traffic information release
Traffic induced
Traffic speed matches the traffic risk
Speed management
Combine traffic signs with real-time traffic information
Traffic signs from, static information, release as the main direction, dynamic information, release iteration
Traffic signs to vehicle-road collaboration, Internet of vehicles, scene evolution

## Slide 16
Intelligent network guide sign
The panel shows the semi-transparent active light emission sign
Deliver the road (space) information
LED Information Screen (digital)
Publish travel time information
LED information screen (light band)
Release road condition information
LED Information Screen (Text)
Release information about traffic events
LED Information Screen (digital)
Release the remaining parking
space information
LED information screen (light band)
Guide the path and road condition
information
The panel shows the semi-transparent active light emission sign
Layout information of the surrounding parking facilities

## Slide 17
Compare this with other release schemes
Display effect, energy consumption, cost and difficulty of installation are better
In the power failure or abnormal conditions, no information can be provided, the lack of redundancy, can not replace the traffic signs. Since the significant, power consumption, cost, installation difficulty is higher
At night or under bad weather conditions, the LED display part can only be recognized, and it is difficult to obtain the layout information
LED display screen (variable intelligence board)
Common sign embedded LED display
Intelligent network guide sign

## Slide 18
Cloud platforms provide data services
  Realize the integration of traffic signs, the whole life cycle management
  realizeData fusionAndCloud policy computing
  Implement the variable information flagDirective issued
  State monitoring
  Data fusion
  Cloud computing
  Strategy synergy
  Decision issuance
  health control
  telecontrol
  incident record
  Can be deployed in a private network
  You can connect with different data sources or other intelligent roadside devices

## Slide 19
applied code
GB 5768.2 Regulations on sign layout, color, font, layout, and variable information sign
GA / 484 LED Road Traffic induced Variable Information signs on local variable information signs
T / CSIA 007 Intelligent Network Guide Sign
Technical standards applicable to intelligent network (guide) signs

## Slide 20
Typical application of intelligent network guide sign
City road scene
Multipath induction of the key nodes
Nanjing · Baixia Park
Wuxi · Smart Transportation Project
Combined with the road signs, continuous induction can be realized at multiple intersections in the road network

## Slide 21
Typical application of intelligent network guide sign
Highway scene
Combined with the location distance sign to provide trip time information
Hebei · Yanchong Expressway
Add traffic induction and traffic control information in the exit signs and bridge signs
Ningxia ·Smart high-speed